## Slide 1
Spectral Features of Argon Light Emission for Next-Generation Rare Event Detectors
Roberto Santorelli
CIEMAT – Madrid
(on behalf of the CIEMAT-DM group)

## Slide 2
R&D program at CIEMAT
+ G. Vera Diaz (PhD student)

## Slide 3
PEN, or similar, polymeric materials. Relatively newer approach:
– Much easier
– Efficiency ≈0.5 (significantly lower than TPB)
Tetraphenyl butadiene (TPB) most popular solution:
– Fast emission, vey high conversion efficiency
– Emanation, degradation…etc
– Large vacuum chamber needed
Wavelength shifting the VUV photons

## Slide 4
Conventional dark matter (and neutrino) Ar detectors integrate the light signal over a wide spectral range!
Wavelength shifting the VUV photons
Is it possible that we miss the potential information
provided by the scintillation wavelength?

## Slide 5
Ionization
e- + Ar  Ar+ + 2e-
Ar+ + Ar + Ar  Ar+2 + Ar Molecular ion
Ar+2 + e-  Ar** + Ar Recombination
Ar** + Ar  Ar* + Ar + heat Excimer
Ar (and Xe) scintillation light
Ar
The superscript v is used to distinguish the vibrational excited states from the purely electronic excitations
(Ar2* with v=0)
h  second continuum at 128 nm (wavelength shifted to 420 nm)
h
Excitation
e- + Ar  Ar* + e-
Ar* + Ar  Arv*2 Excimer formation
(bound diatomic molecules in the exc. state)
Arv*2 + Ar  Ar2* + Ar Relaxation
Ar2*  Ar + Ar + h Radiative de-exc.
and dissociation

## Slide 6
Where does this light come from?
This is not completely true:
We do see some light even without wavelength-shifting the photons to 420 nm
What is the impact of this composite spectral emission?

## Slide 7
High pressure and low pressure regions decoupled.
Three wavelength regions defined with different PMT models and filters.
The Octopus detector

## Slide 8
PMT | Model | Sensitivity Range [nm]
UV2 | R6835 | [115-160]
UV3 | R7378 | [160-visible]
TPB | R6095+TPB evaporated | [110-visible]

## Slide 9
Ar scintillation at 1 bar (Am-241)
Eur. Phys. J. C 81, 622

## Slide 10
Ar scintillation at 1 bar (Am-241)
The TPB pulse is the sum of the UV2 and UV3 signals
Average pulse over 3 x 104 events using 241Am source

## Slide 11
Mechanisms leading to scintillation mainly in the region 180-300 nm are grouped under the generic denomination of “3rd continuum” (despite it is very plausible that a number of different species contribute)
Two leading hypothesis for the precursors: doubly ionized (Ar++) and excited (Ar+*) ions
No quantitative predictions up to date from molecular physics:
Our data confirm that the “3rd continuum” is field independent.
“Higher order” continuum
[1] T.Heindl et al., “The scintillation of liquid argon”, Europhys.Lett. 91 62002s (2010).

## Slide 12
Fast component vs pressure and El. field
The third continuum dominates signal over the first 90 ns up to 5 bar (and continues to be an important contribution for higher pressures). Almost no dependence on P
The UV3 signal is not affected by an external electric field
Phys. Rev. Lett. 33,
1365 (1974)
The excimer formation time strongly depends on P

## Slide 13
Emission constants

## Slide 14
Electroluminescence studies
Small TPC designed to study the UV component (λ > 160 nm) of the EL light in Ar
Pin< 9e-5 mbar (before filling), Pout<5e−4 mbar (constant)
Alphagaz™-2 (6.0 purity), flux 1 slm, Pin=(1.08 ±0.02) bar
CAEN DT5730SB ADC 14-bit, 500 MS/s, 2 V
Ldrift=2.26 cm, LEL= 0.47 cm
Edrift= 266 V/cm, EEL= 1.69 kV/cm
241Am α source
(≈5.5 MeV, ≈ 90 Bq,
collimated)

## Slide 15
Fields OFF (S1-pulse @1 bar)
“UV3” light (VUV photons with wavelength > 160 nm) detected with this upgraded setup
Features consistent with the previous results
τPMT1 = 3.11 ± 0.11 μs
τPMT2 = 3.19 ± 0.15 μs

## Slide 16
Fields ON (El-pulse @ 1 bar)
We do see “UV3” light In the electroluminescence signal
UV3 photons emission fraction: (10.44 ± 0.23)%.
EL light

## Slide 17
Fields ON EL-average pulse (1 bar)
[ns]
[ns]
[ns]
[ns]

## Slide 18
Fields ON EL-average pulse (1 bar)
PRELIMINARY
PRELIMINARY

## Slide 19
Event characterization

## Slide 20
New detectors in preparation

## Slide 21
Conclusions
Conventional Ar/Xe detectors are built with fast light detection devices coupled with photon wavelength-shifters that integrate the light signal over a wide spectral range
Potential information provided by the scintillation wavelength?
Fast emission in GAr detected, different from the standard second continuum and consistent with the third continuum
We have established that the argon second and third continuum can be distinguished experimentally by means of sensors with different spectral sensitivities
We have proved that this fast light emission is also present in the EL light
New studies on going (larger chambers, LAr studies)

## Slide 22
谢谢大家！

## Slide 23
BONUS SLIDES