## Slide 1: Status and Prospects of the TRIDENT Neutrino Telescope
...(and its design)
Iwan Morton-Blake
On behalf of the TRIDENT collaboration
Tsung-Dao Lee Institute,
Shanghai Jiao Tong University
TAUP 2025 in Xichang, China

## Slide 2
Solar
Reactor
Atmospheric
Geoneutrinos
Supernova
1010
1
10-20
10-10
keV GeV PeV
Flux [cm-2 s-1 sr-1 MeV-1]
Active galactic nucleus, cosmological sources
Exotic Searches
Neutrino Sources
~70 years experience in neutrino measurement!
This Talk
Detectors have been steadily growing to reach the desired precision/fluxes
Searches for astrophysical sources are no exception to the rule

## Slide 3
200
kgs
23 kilotons
1 kiloton
190
kilotons
0.1 km3
1 km3
3 kilotons
1 kiloton
They grow up so fast 🥲
…

## Slide 4: IceCube
Hot Water Drilling
Single Downward 10” PMT
Cofield, C. IceCube catches high-energy neutrino oscillations. Nature (2012).
IceCube Collaboration, R. Abbasi et al., Nucl. Instrum. Meth. A700 (2013) 188–220
~1km3 footprint

## Slide 5: IceCube
(Some) highlights from the last 12 years
Detect extraterrestrial high-energy diffuse neutrino flux
Evidence for neutrino emission from a flaring blazar
Glashow resonance event at 2.3σ
Neutrino emission from active galaxy NGC 1068 reaches 4σ
Galactic plane >TeV neutrinos observed at a 4.5σ
Science. 342 6161 (2013)
Science. 361 6398 (2018)
Nature 591 220-224 (2021)
Science 378 538-543 (2022)
Science 380 1338 (2023)

## Slide 6: TRIDENT  ~10km3
Experimental goals:
Rapidly discover neutrino sources
Sensitivity to all flavors

## Slide 7: TRIDENT  ~10km3
Experimental goals:
Rapidly discover neutrino sources
Sensitivity to all flavors
Want to optimize for both goals simultaneously
Detector Design:
Bigger is better?

## Slide 8
TRIDENT
Expeditions to Sea
R&D
for Technology + Deployment
Present day
First String Deployment: Phase -1
“Prototype Testing for TRIDENT: In-Situ Performance of Multi-PMT Optical Modules” – Fuyudi Zhang
“TRIDENT: Advancing Future Deep-sea Neutrino Observatory” – Xin Xiang
This talk
Full TRIDENT Array
TRIDENT Timeline

## Slide 9: Event interaction types
decay
(τ decay can also produce muons)
Neutral-Current
Charged-Current
Muon tracks
Cascades

## Slide 10: All-Flavour Detection
Track angular resolution
TRIDENT Simulation
TRIDENT Simulation
Cascade angular resolution
Simulated Track-like event in TRIDENT
Simulated Cascade-like event in TRIDENT
~0.1°
~2°

## Slide 11: All-rounder detector
+ Excellent for pointing  point source discovery
+ Detection volume > Detector volume
Partial energy deposition within detector
Atmospheric muons : strong down-going background
+ , detection channels
+ Energy deposition within detector
+ Low atmospheric muon and neutrino background
Poorer pointing  + But, good for diffuse sources
Atmospheric muons strong background
Difficult to optimize for all types events of all energies!

## Slide 12
Experimental goals:
Rapidly discover neutrino sources
Sensitivity to all flavors
Point source sensitivity/Discovery potential vs declination,
with tracks
TRIDENT neutrino flavour ratio sensitivity
with tracks, cascades and double-pulse tau identification
Combine both goals into a single figure of merit?
(Publication in preparation)
Nature Astronomy 7, 1497–1505 (2023)
“Real-time Optical Calibration Strategy and Astrophysical Tau Neutrino Identification in Water-based Next-generation Neutrino Telescopes” W. Tian, PhD Thesis

## Slide 13
Physics
Cost + Engineering
An experiment’s design must be lead by physics
limited by engineering and cost

## Slide 14: Neutrino Telescope Design
Location
2) Optical Modules
3) String Layout / Volume

## Slide 15: Detector Design – Location
1:25 scale string models in SJTU Ship-towing tank
South China Sea
Near the equator
3.5 km deep
Large, flat plane
TRIDENT
YongXing Island
180km
480km
540km
Sanya
Hong Kong
TRIDENT sensitive viewing region:
Low seacurrents, bioactivity
“MuonSLab: A plastic scintillator based detector for muon measurement in the deep ocean”
Low atmospheric muon rate

## Slide 16: Detector Design – hDOM
Hybrid Digital Optical Module
Hybrid: PMTs + SiPMs
JINST 19 (2024) 06, P06011
JINST 19 (2024) 05, P05040
“A Cost Effective Optimization of the hybrid-DOM Design for TRIDENT”
SiPMs
 Fine timing resolution
Fills spaces between the PMTs, extra sensitivity
SiPM arrays aids in calibration
PMTs
Fine timing resolution (TTS FWHM ~1.8 ns)
High quantum efficiency >30% at 400nm
Balance design with:
Reduction of backgrounds:
e.g. 40K & PMT Dark noise
Cost & Power consumption
Additional low energy physics

## Slide 17: Detector Design – hDOM
“A Cost Effective Optimization of the hybrid-DOM Design for TRIDENT”
3-inch PMT hDOM design
31 3” PMTs
24 SiPMs
(4x8 array)
4-inch PMT hDOM design
19 4” PMTs
5 SiPMs
(8x8 array)
Check / compare performances for various designs:
e.g. neutrino detection efficiency + angular resolution
Efficient light collection is important (as expected)

## Slide 18: Detector Design - Geometry
Nature Astronomy volume 4, p913–915 (2020)
KM3NeT
Baikal GVD
P-ONE
5th International Symposium on Cosmic Rays and Astrophysics, Zhan-Arys Dzhilkibaev
Lake Louise Winter Institute 2025,
Agustín Sánchez Losa
Nature Astronomy 7, p1497–1505 (2023)

## Slide 19: Detector Geometry : String Spacing
Given N number of strings, how should they be arranged?
(looking down on detector)
Can quickly expand detector volume
Must balance volume with detection efficiency
Deployment difficulties, strings may tangle if too close!
Increasing string spacing

## Slide 20: Detector Geometry : String Height
Given N number of strings, how should they be arranged?
(looking side-on)
Improve horizontal event detection cross-section
Deployment/maintenance issues if too tall!
Increasing string height

## Slide 21: Detector Geometry : Clustering
Given N number of strings, how should they be arranged?
(looking top-down)
Deployment/maintenance benefits
Low energy threshold
Miss events in cluster-cluster gaps
More edge events
Equal volume,
More severe clustering

## Slide 22
1) Source neutrino flux
Energy + Direction
2) Forced Interaction near the detector
Event weighting  Earth propagation, cross sections, oscillation
3) Deep Inelastic Scattering (CORSIKA8[1,2])
Neutral and Charged Current interactions
Particle production
6) Detector response
Photoelectron generation, 40K + dark noise mixing
4) Lepton, hadron propagation (CORSIKA8/Geant4[3])
5) Cherenkov photon generation + propagation (Geant4/Optix[4])
Scattering, absorption, dispersion
7) Electronics response, Triggering, data cleaning
TRIDENTSim
Signal photons +
noise + radioactivity
time

## Slide 23: Comparing Geometries
“Reference” geometry
Calculate neutrino source discovery potential for each design
Include TRIDENT-site measured optical conditions, atmospheric backgrounds, hDOM backgrounds
Compare versus “Reference” geometry:
Average string spacing ~ 100m
String height ~ 600m
“A multi-cubic-kilometre neutrino telescope in the western Pacific Ocean”
Nature Astronomy (2023)

## Slide 24: Track Performance vs Detector Size
TRIDENT Simulation
TRIDENT Simulation
Big sparse detector : More (fewer) high (low) energy tracks Worse direction resolution
Small dense detector : Fewer (~equal) high (low) energy tracks Better direction resolution
Relative signal event rate
Rel. pointing resolution
Better
Dense 3km3  Sparse 16km3
Track-like events

## Slide 25: Cascade Performance vs Detector Size
TRIDENT Simulation
TRIDENT Simulation
Relative Signal Event Rate
Rel. Pointing Resolution
Better
Dense 3km3  Sparse 16km3
Cascade-like events
Big sparse detector : More (fewer) high (low) energy cascades Worse direction resolution
Small dense detector : Fewer (~equal) high (low) energy cascades Better direction resolution

## Slide 26: Source Discovery Potential
Assuming the “standard” geometry takes 5 years to discover a given source
How much slower/faster can each geometry discover same source?
Bigger detector is not necessarily better
Worse at low energies tracks and cascades:
Worse at high energies tracks and cascades:
Dense detector favours low energy events
TRIDENT Simulation
“hard” source
“soft” source

## Slide 27: Source Discovery Potential – String Clustering
Clusters of strings shows poorer performance for all channels, except for low energy cascades.
However, physics must be weighed against deployment & maintenance cost, safety
TRIDENT Simulation

## Slide 28: Source Discovery Potential – Optical properties
While geometry choice is significant,
water optical properties are essential!
 e.g. attenuation length can have larger impact than geometry choices
Photon detection efficiency should lead the design of a detector.
i.e. ongoing/future measurements at site and in TRIDENT Phase-1 will influence the final design choice
TRIDENT Simulation

## Slide 29: Conclusion
TRIDENT is an upcoming neutrino telescope expected to reach next-generation size and performance
Phase-1 of the experiment expected to start next year
TRIDENT’s design is optimised directly via its physics goals:
 Rapid source discovery and all-flavour detection
Bigger does not necessarily mean better:
 Event rate must be balanced with reconstruction quality.
Optical properties play a significant role and should lead design

## Slide 30: Team efforts
When they’re not building telescopes,
they’re contributing to the work shown here!
Weilun Huang
Dr. Fan Hu
Fuyudi Zhang
Qichao Chang
Dr. Wei Tian
+ …

## Slide 31: Backup

## Slide 32: Optimisation: Many degrees of freedom
Flavor ratio
Probe acceleration mechanisms
Oscillation over astro. baselines
Tests of BSM physicss
Source discovery
Rapid discovery of multiple neutrino sources
Understand energy spectra
Low energy neutrinos
Core-collapse neutrino sensitivity
Dark matter searches
Astrophysical neutrino detection
Understanding our Galactic Centre
TRIDENT work in progress
Geophysics:
Modelling of Earth’s matter density

## Slide 33
What are our individual and collective physics goals in each experiment?
Fast discovery of potential sources?
Once discovered, how do we deepen our understanding of sources?
What exactly is each detector’s target energy range?
P-ONE
KM3NeT
Baikal GVD
IceCube Gen 2
TRIDENT
HUNT
NEON
Looking Ahead

## Slide 34
Cosmic rays
Cosmic neutrinos
~Kilometers of ice/water + air above
High-energy neutrinos can be absorbed in the Earth
Carry out all-sky search for potential sources
Muon track ~O(km) long
Cascade ~O(m) long
Atmospheric μ + ν
TRIDENTSim
δ
φ

## Slide 35
TRIDENT Sensitivity + Discovery Potential
90% confidence-level median sensitivity (dashed-dot lines)
5σ discovery potential (solid lines)
declination
(source position in the sky)