## Slide 1: Joint Self-Collimation Compton Imaging: A High-Resolution and High-SNR Solution for Wide-Energy SPECT
Peize Li1, Linxin Lei1, Xingchun Zheng1, Zhenlei Lyu1, Zerui Yu1, Linkang Liu1, Rutao Yao2, Tianyu Ma1*
Department of Engineering Physics, Tsinghua University
#72
Notes: 1、有一些页还在读页面上的文字，还没有完全熟练，尤其前面的introduction部分
2、有几个逻辑过渡还比较生硬

## Slide 2
Introduction
High energy SPECT is of great importance
Peize Li. Joint Self-Collimation Compton Imaging #72
100
600
Energy/keV
99mTc
111In
123I
200
300
400
500
High Energy
Medium Energy
Low Energy
Spans a broad spectrum of diseases with diverse radiotracers
Conventional SPECT tracers emits low to medium energy photons
SPECT is a widely-used molecular imaging technology
99mTc-MIBI cardiac perfusion imaging
99mTc-MDP bone metastasis imaging
99mTc-ECD brain perfusion imaging
123I - MIBG Sympathetic nerve imaging
Notes: As is widely known, SPECT is able to be applied to many diseases with varies radiotracers.
Here we show some commonly used radiopharmaceuticals.

## Slide 3
Introduction
High energy SPECT is of great importance
Peize Li. Joint Self-Collimation Compton Imaging #72
100
600
Energy/keV
99mTc
177Lu
111In
123I
131I
225Ac
200
300
400
500
High Energy
Medium Energy
Low Energy
Radiotherapeutic isotopes emit medium to high-energy photons
225Ac/177Lu-PSMA/DOTATATE, 131I…
For patient selection & response assessment
SPECT is especially valuable in the era of theranostics
Spans a broad spectrum of diseases with diverse radiotracers
Conventional SPECT tracers emits low to medium energy photons
SPECT is a widely-used molecular imaging technology
99mTc-MIBI cardiac perfusion imaging
99mTc-MDP bone metastasis imaging
99mTc-ECD brain perfusion imaging
123I - MIBG Sympathetic nerve imaging

## Slide 4
Introduction
High energy SPECT is of great importance
Peize Li. Joint Self-Collimation Compton Imaging #72
Radiotherapeutic isotopes emit medium to high-energy photons
225Ac/177Lu-PSMA/DOTATATE, 131I…
For patient selection & response assessment
SPECT is especially valuable in the era of theranostics
100
600
Energy/keV
99mTc
177Lu
111In
123I
131I
225Ac
200
300
400
500
High Energy
Medium Energy
Low Energy
18F
Spans a broad spectrum of diseases with diverse radiotracers
Conventional SPECT tracers emits low to medium energy photons
SPECT is a widely-used molecular imaging technology
99mTc-MIBI cardiac perfusion imaging
99mTc-MDP bone metastasis imaging
99mTc-ECD brain perfusion imaging
123I - MIBG Sympathetic nerve imaging
Has promising potential for intraoperative imaging applications
SPECT can be expanded to image positron-emission isotopes
Notes: 讲的时候提一下核素名称。第一个标题要说出来。low~ to ~medium 着重说，放慢速度强调
flexible

## Slide 5
Introduction
High energy SPECT is challenging
Peize Li. Joint Self-Collimation Compton Imaging #72
Collimator
Detector
FOV
Parallel hole collimator
Pin-hole collimator
Parallel-hole collimator: Design of collimator introduces intrinsic resolution – sensitivity trade-off
Pin-hole collimator: Improves resolution by reducing distance to object. FOV - resolution – sensitivity trade-off
Challenge in performance balance
Notes: For conventional SPECT equiped with mechanical collimator, there is great challenge to balance performance

## Slide 6
Introduction
High energy SPECT is challenging
Peize Li. Joint Self-Collimation Compton Imaging #72
Collimator
Detector
FOV
Parallel hole collimator
Pin-hole collimator
Energy / keV | Lead thickness needed for 90% photon attenuation | Scattering proportion in GAGG(Ce)
140 | 0.92 mm | 15.77%
208 | 2.38 mm | 33.87%
364 | 7.97 mm | 66.12%
440 | 11.10 mm | 74.76%
511 | 13.98mm | 80.21%
Parallel-hole collimator: Design of collimator introduces intrinsic resolution – sensitivity trade-off
Pin-hole collimator: Improves resolution by reducing distance to object. FOV - resolution – sensitivity trade-off
Challenge in performance balance
Higher photon energy leads to stronger penetration → degraded resolution
Stronger collimator wall penetration

## Slide 7
Introduction
High energy SPECT is challenging
Peize Li. Joint Self-Collimation Compton Imaging #72
Parallel-hole collimator: Design of collimator introduces intrinsic resolution – sensitivity trade-off
Pin-hole collimator: Improves resolution by reducing distance to object. FOV - resolution – sensitivity trade-off
Challenge in performance balance
Higher photon energy leads to stronger penetration → degraded resolution
Stronger collimator wall penetration
Collimator
Detector
FOV
Parallel hole collimator
Pin-hole collimator
Reduced sensitivity and introduced noise → low SNR
Significantly increased scatter in detector/collimator
Energy / keV | Lead thickness needed for 90% photon attenuation | Scattering proportion in GAGG(Ce)
140 | 0.92 mm | 15.77%
208 | 2.38 mm | 33.87%
364 | 7.97 mm | 66.12%
440 | 11.10 mm | 74.76%
511 | 13.98mm | 80.21%

## Slide 8
Introduction
Self-collimation (SC) SPECT
Peize Li. Joint Self-Collimation Compton Imaging #72
Obtain collimation by the mutual shielding between detectors
Existing self-collimation gamma cameras can achieve super high resolution without losing sensitivity for 99mTc
For low energy photons: significant performance improvement
Multi-layer
Detectors
Collimator
FOV
SC-SPECT
MIP, 30 Views
GE NM670 (LEHR)
MIP, 60 Views
3D thyroid 99mTc imaging
Mouse bone 99mTc-MDP scintigraphy

## Slide 9
Introduction
Self-collimation (SC) SPECT
Peize Li. Joint Self-Collimation Compton Imaging #72
Obtain collimation by the mutual shielding between detectors
Existing self-collimation gamma cameras can achieve super high resolution without losing sensitivity for 99mTc
For low energy photons: significant performance improvement
Multi-layer
Detectors
Collimator
FOV
Severe scintillator penetration → reduced collimatin effect
Increased Compton-scattering events → deteriorated image quality
For high energy photons: degraded performance
SC-SPECT
MIP, 30 Views
GE NM670 (LEHR)
MIP, 60 Views
3D thyroid 99mTc imaging
Mouse bone 99mTc-MDP scintigraphy

## Slide 10
Introduction
Self-collimation (SC) SPECT
Peize Li. Joint Self-Collimation Compton Imaging #72
Obtain collimation by the mutual shielding between detectors.
Existing self-collimation gamma cameras can achieve super high resolution without losing sensitivity for 99mTc.
For low energy photons: significant performance improvement
Multi-layer
Detectors
Collimator
FOV
Severe scintillator penetration → reduced collimatin effect
Increased Compton-scattering events → deteriorated image quality
For high energy photons: degraded performance
Joint Self-Collimation Compton Imaging (JSCC): combine self-collimation and Compton imaging
SC-SPECT
MIP, 30 Views
GE NM670 (LEHR)
MIP, 60 Views
3D thyroid 99mTc imaging
Mouse bone 99mTc-MDP scintigraphy

## Slide 11
Joint Self-Collimation Compton Imaging
Introduction
Peize Li. Joint Self-Collimation Compton Imaging #72
Tsinghua University
JSCC gamma camera schematic diagram
Multi-layer Self-collimation Detectors with metel blocks
Probability Distribution
FOV
Scintillator Block
Metal Block
(Both as Collimator)
Notes: Lets start with a self-collimation gamma camera desing with multi-layer detectors of mosaic-patterns 说明四层结构的自准直相机的构造

## Slide 12
Joint Self-Collimation Compton Imaging
Introduction
Peize Li. Joint Self-Collimation Compton Imaging #72
Tsinghua University
An ideally collimated event
Probability Distribution
FOV
Scintillator Block
Metal Block
Source
(Both as Collimator)

## Slide 13
Joint Self-Collimation Compton Imaging
Introduction
Peize Li. Joint Self-Collimation Compton Imaging #72
Tsinghua University
Multiple possible photon paths induced multiplexing -> reduce SNR
Probability Distribution
FOV
Scintillator Block
Metal Block
Source
(Both as Collimator)
Multiplexed Photon Path
Multiplexed Photon Path
True Photon Path

## Slide 14
Joint Self-Collimation Compton Imaging
Introduction
Peize Li. Joint Self-Collimation Compton Imaging #72
Tsinghua University
High photon energy induced stronger penetration -> further deteriorate SNR
Probability Distribution
FOV
Scintillator Block
Metal Block
Source
(Both as Collimator)
Multiplexed Photon Path
Multiplexed Photon Path
True Photon Path

## Slide 15
Joint Self-Collimation Compton Imaging
Introduction
Peize Li. Joint Self-Collimation Compton Imaging #72
Tsinghua University
A Compton scattering event
Probability Distribution
FOV
Scintillator Block
Metal Block
Scattered photon
Source
(Both as Collimator)
Multiplexed Photon Path
Multiplexed Photon Path
True Photon Path

## Slide 16
Introduction
Peize Li. Joint Self-Collimation Compton Imaging #72
Tsinghua University
Compton cone brings additional directional information
Joint Self-Collimation Compton Imaging
Probability Distribution
Compton Cone
FOV
Multiplexed Photon Path
Multiplexed Photon Path
Scintillator Block
Metal Block
Scattered photon
Source
(Both as Collimator)
True Photon Path
Notes: 说Compton Cone 同时展示出它

## Slide 17
Introduction
Peize Li. Joint Self-Collimation Compton Imaging #72
Tsinghua University
Enhance imaging quality through joint imaging
Joint Self-Collimation Compton Imaging
Probability Distribution
Compton Cone
Scintillator Block
Metal Block
Scattered photon
Source
(Both as Collimator)
Intercepted zone
Multiplexed Photon Path
Multiplexed Photon Path
FOV

## Slide 18
Methods
Proof-of-concept Experiment
Peize Li. Joint Self-Collimation Compton Imaging #72
Source/
Phantom
Self-collimation
Gamma Camera
1
2
3
4
100mm
50mm
50mm
50mm
50mm
FOV
588 holes with 3mm diameter
Tungsten Coded aperture plate
Layer1~Layer3
512 Mosaic-patterned GAGG(Ce) scintillator
Scintillator Size: 3mm×3mm×6mm
Layer4
4096 Densely packed GAGG(Ce) scintillator
Scintillator Size: 2mm×2mm×6mm
Proof-of-concept on an existing self-collimation gamma camera design
Notes: To validate the JSCC method
Since this gamma camera was not specifically designed for JSCC, there are many aspects that still require optimization.

## Slide 19
Experiment: Energy Calibration & Event Selection
Peize Li. Joint Self-Collimation Compton Imaging #72
Energy resolution: 13% FWHM at 511 keV
Select single-photon events from [460 560] keV window
Sort coincidence events with 50 ns window
Select Compton events from [460 600] keV window
Methods
Compton Events
E1+E2 ≈ 511keV
E1
E2
Notes: We set a time window to acquire Compton coincidence events, and defined specific energy windows for the selection of two types of events.
加一个表示E1 & E2的图？

## Slide 20
2 s
511 keV
10 mCi
0.2 s
SC
JSCC
JSCC
SC
Results
Experimental Imaging Results
Peize Li. Joint Self-Collimation Compton Imaging #72
1 s
511 keV
3.5 mCi
0.5 s
0.25 s
0.1 s
100 mm
24 mm
20 mm
Notes: 一页放所有实验结果，给出来single-photon和Compton events的比例，this is not an optimized porpotion

## Slide 21
2 s
511 keV
10 mCi
0.2 s
SC
JSCC
JSCC
SC
Results
Experimental Imaging Results
Peize Li. Joint Self-Collimation Compton Imaging #72
1 s
511 keV
3.5 mCi
0.5 s
0.25 s
0.1 s
100 mm
24 mm
20 mm
Low Compton events proportion: 2.76%
Due to none-optimized system design
Notes: 一页放所有实验结果，给出来single-photon和Compton events的比例，this is not an optimized porpotion

## Slide 22
Methods
Monte-Carlo Simulation Configuration
Peize Li. Joint Self-Collimation Compton Imaging #72
Layer | Block Size | Number of GAGG(Ce) Blocks | Number of tungsten Blocks
1 | 3×3×3 mm3 | 256 | 256
2 |  |  | 
 |  | 384 | 168
3 |  |  | 
 |  | 512 | 88
4 | 2×2×6 mm3 | 4096 | 0
To improve sensitivity:
Remove the coded aperture plate
To balance sensitivity and resolution:
Place the metal blocks inside the detector layers
more metal on front layers, more scintillator on lateral layers
To reduce intra-scintillator Compton scattering:
Crystal size from 3mm×3mm×6mm to 3mm×3mm×3mm
Optimized JSCC gamma camera design
Notes: 三个点动画分别出来

## Slide 23
Energy Resolution: 10% at 662keV
Evaluate SNR
Evaluate spatial resolution
NEMA Body Phantom
Hot-rod Phantom
Peize Li. Joint Self-Collimation Compton Imaging #72
2.8 mm
3.4 mm
4.0 mm
4.6 mm
5.8 mm
5.2 mm
10 mm
13 mm
17 mm
22 mm
28 mm
37 mm
50 mm
Hot-rod: Background = 10:1
290 mm
220 mm
Methods
Geant4 Monte Carlos simulation
Isotope | Energy | Energy Window (Single Events)
18F | 511 keV | [460 560]
Monte-Carlo Simulation Phantoms
Notes: 没必要提及225Ac和18F核素的应用

## Slide 24
SC
Results
Simulation: Hot-rod Phantom
Peize Li. Joint Self-Collimation Compton Imaging #72
JSCC
90 min
511 keV
1 mCi
2.8 mm hot rods resolvable for both JSCC and SC in high-count condition
2.8 mm
3.4 mm
4.0 mm
4.6 mm
5.8 mm
5.2 mm
Line Profile
Chart: 
1.4 7.0 13.6 19.2
Relative Coordinates / mm
SC
JSCC
Notes: significantly surpasses conventional SPECT, comparable to the level of PET

## Slide 25
Results
Simulation: NEMA Body Phantom
Peize Li. Joint Self-Collimation Compton Imaging #72
9 min
511 keV
1 mCi
2 min
10 s
10 13 17 22 28 37
Diameter / mm
10 mm
13 mm
17 mm
22 mm
28 mm
37 mm
50 mm
SC
JSCC
Chart: 
| 10mm | 13mm | 17mm | 22mm | 28mm | 37mm
SC | 2.9 | 2.54 | 4.34 | 6.73 | 6.33 | 7.16
JSCC | 3.7 | 7.56 | 8.19 | 11.95 | 14.17 | 15.12
Chart: 
| 10mm | 13mm | 17mm | 22mm | 28mm | 37mm
SC | 0.42 | 0.17 | 2.08 | 3.4 | 3.26 | 2.73
JSCC | 1.05 | 3.13 | 5.4 | 6.93 | 7.6 | 10.52
JSCC significantly improves SNR, especially in low-count conditions.
CNR(Contrast-to-Noise Ratio)
Chart: 
| 10mm | 13mm | 17mm | 22mm | 28mm | 37mm
SC | 4.22 | 6.16 | 8.01 | 7.55 | 7.92 | 8.91
JSCC | 5.84 | 9.22 | 10.89 | 12.89 | 15.34 | 16.34
Notes: this advantage becomes more prominent under

## Slide 26
CNR(Contrast-to-Noise Ratio)
Results
Simulation: NEMA Body Phantom
Peize Li. Joint Self-Collimation Compton Imaging #72
9 min
511 keV
1 mCi
2 min
10 s
10 13 17 22 28 37
Diameter / mm
10 mm
13 mm
17 mm
22 mm
28 mm
37 mm
50 mm
SC
JSCC
Chart: 
| 10mm | 13mm | 17mm | 22mm | 28mm | 37mm
SC | 2.9 | 2.54 | 4.34 | 6.73 | 6.33 | 7.16
JSCC | 3.7 | 7.56 | 8.19 | 11.95 | 14.17 | 15.12
Chart: 
| 10mm | 13mm | 17mm | 22mm | 28mm | 37mm
SC | 0.42 | 0.17 | 2.08 | 3.4 | 3.26 | 2.73
JSCC | 1.05 | 3.13 | 5.4 | 6.93 | 7.6 | 10.52
JSCC significantly improves SNR, especially in low-count conditions.
JSCC more clearly resolve cold-rods.
Chart: 
| 10mm | 13mm | 17mm | 22mm | 28mm | 37mm
SC | 4.22 | 6.16 | 8.01 | 7.55 | 7.92 | 8.91
JSCC | 5.84 | 9.22 | 10.89 | 12.89 | 15.34 | 16.34
Notes: this advantage becomes more prominent under

## Slide 27
Peize Li. Joint Self-Collimation Compton Imaging #72
Methods
From 2D to 3D, High-energy to Wide-energy
Planar, High-energy Imaging
600
18F
High Energy
500
Volumetric, Wide-energy Imaging
100
600
200
300
400
500
High Energy
Medium Energy
Low Energy
99mTc
111In
123I
177Lu
131I
225Ac
18F
Is the JSCC method effective for more complex conditions?
Notes: this advantage becomes more prominent under

## Slide 28
Peize Li. Joint Self-Collimation Compton Imaging #72
Methods
Monte-Carlo Simulation Configuration
300 mm
200 mm
60 mm
60 Rotations
JSCC SPECT Detector (Proposed)
Parallel-hole SPECT (Comparison)
Area: 270 mm × 135 mm
Lateral stitching of two planar imaging JSCC gamma cameras
Area: 270 mm × 135 mm
Scintillator: NaI, 10 mm Thickness
Collimator holes:
  Diameter: 2.5 mm,
  Septal thickness: 3.4 mm
  Hole length: 50.5 mm
Cylinder FOV
Notes: this advantage becomes more prominent under

## Slide 29
Peize Li. Joint Self-Collimation Compton Imaging #72
Methods
Monte-Carlo Simulation Phantoms
30 mm
240 mm
10 mm
14 mm
18 mm
22 mm
26 mm
30 mm
22 mm
19 mm
16 mm
7 mm
13 mm
10 mm
Height: 30 mm
30 mm
240 mm
8 mm
10 mm
12 mm
14 mm
16 mm
18 mm
15 mm
13 mm
11 mm
5 mm
9 mm
7 mm
Height: 30 mm
Contrast Phantom
Hot-rod Phantom
Phantoms for 511 keV
Contrast Phantom
Hot-rod Phantom
Phantoms for 140 keV
250 mm
180 mm
Transverse
Coronal
Sagittal
60 mm
Hoffman Phantom
Notes: this advantage becomes more prominent under

## Slide 30
CNR(Contrast-to-Noise Ratio)
Results
Simulation – 511 keV
Peize Li. Joint Self-Collimation Compton Imaging #72
20 min
511 keV
1 mCi
2 min
30 s
10 14 18 22 26 30
Diameter / mm
Parallel-hole
JSCC
Chart: 
| 10mm | 13mm | 17mm | 22mm | 28mm | 37mm
SC | -0.21596 | 1.658 | 2.9276 | 2.06 | 4.4469 | 4.957
JSCC | 0.86661 | 1.7135 | 3.9048 | 6.9508 | 8.6092 | 8.9101
Chart: 
| 10mm | 13mm | 17mm | 22mm | 28mm | 37mm
SC | 0.032657 | 0.76661 | 2.124 | 1.6893 | 2.3121 | 1.5994
JSCC | 0.22508 | 0.12789 | 1.4475 | 2.0428 | 4.0444 | 6.243
JSCC significantly improves SNR, especially in low-count conditions.
Chart: 
| 10mm | 13mm | 17mm | 22mm | 28mm | 37mm
SC | 0.37929 | 4.1715 | 6.0112 | 8.5582 | 7.9827 | 9.3084
JSCC | 2.3308 | 4.4018 | 8.7567 | 9.1552 | 10.9171 | 10.4872
10 mm
14 mm
18 mm
22 mm
26 mm
30 mm
A
A'
B
B'
A
A'
B
B'
A
A'
B
B'
A – A'
A – A'
A – A'
B – B'
B – B'
B – B'
Notes: this advantage becomes more prominent under

## Slide 31
10 h
511 keV
1 mCi
4 min
JSCC
Parallel-hole
Results
Simulation – 511 keV
Peize Li. Joint Self-Collimation Compton Imaging #72
20 min
511 keV
1 mCi
30 s
JSCC
Parallel-hole
22 mm
19 mm
16 mm
7 mm
13 mm
10 mm
Transverse
Coronal
Sagittal
Transverse
Coronal
Sagittal
Transverse
Coronal
Sagittal
Transverse
Coronal
Sagittal
JSCC achieves better resolution and is better able to restore details of complex structures.
Notes: this advantage becomes more prominent under

## Slide 32
CNR(Contrast-to-Noise Ratio)
Results
Simulation – 140 keV
Peize Li. Joint Self-Collimation Compton Imaging #72
20 min
140 keV
1 mCi
2 min
30 s
8 10 12 14 16 18
Diameter / mm
Parallel-hole
JSCC
Chart: 
| 10mm | 13mm | 17mm | 22mm | 28mm | 37mm
SC | 1.3875 | 1.4918 | 2.9101 | 6.0525 | 6.7753 | 10.4217
JSCC | 4.1944 | 3.3946 | 6.1074 | 9.7361 | 11.0501 | 13.88
Chart: 
| 10mm | 13mm | 17mm | 22mm | 28mm | 37mm
SC | 1.5114 | 1.5276 | 1.5893 | 2.9079 | 5.1707 | 3.6698
JSCC | 1.7889 | 2.2798 | 3.1367 | 5.9437 | 7.449 | 10.7598
JSCC significantly improves SNR, especially in low-count conditions.
Chart: 
| 10mm | 13mm | 17mm | 22mm | 28mm | 37mm
SC | 4.6939 | 5.0177 | 5.3398 | 10.691 | 12.4588 | 15.0486
JSCC | 11.1217 | 10.2785 | 11.1818 | 13.9791 | 14.5582 | 16.4002
A
A'
B
B'
A
A'
B
B'
A
A'
B
B'
A – A'
A – A'
A – A'
B – B'
B – B'
B – B'
8 mm
10 mm
12 mm
14 mm
16 mm
18 mm
Notes: this advantage becomes more prominent under

## Slide 33
Transverse
Coronal
Sagittal
Transverse
Coronal
Sagittal
Transverse
Coronal
Sagittal
Transverse
Coronal
Sagittal
10 h
140 keV
1 mCi
4 min
JSCC
Parallel-hole
Results
Simulation – 140 keV
Peize Li. Joint Self-Collimation Compton Imaging #72
20 min
140 keV
1 mCi
30 s
JSCC
Parallel-hole
15 mm
13 mm
11 mm
5 mm
9 mm
7 mm
JSCC also achieved significantly better image quality at low energy.
Notes: this advantage becomes more prominent under

## Slide 34
Conclusion
Peize Li. Joint Self-Collimation Compton Imaging #72
Builds upon the high-resolution and high-sensitivity advantages of self-collimation
Incorporates Compton events to reduce multiplexing and improve SNR
Suitable for wide-energy SPECT
Proposed Joint Self-Collimation Compton Imaging concept:
Continue building and refining the dedicated JSCC gamma camera
Further optimize image reconstruction algorithms
Future work
Validate JSCC method on an existing self-collimation gamma camera
Proof-of-concept experiments:
Through simulation, JSCC demonstrates both high resolution and high SNR
Shows strong potential for improving wide energy SPECT imaging performance
Proposed an optimized JSCC gamma camera design:

## Slide 35
Acknowledgment
Peize Li. Joint Self-Collimation Compton Imaging #72
Engineering team
Tsinghua Nuclear Imaging Physics Group
Rutao Yao,
SUNY at Buffalo

## Slide 36: Thank you for listening！
Large animal SPECT/CT, SNMMI 2018 SS43 No. 362