## Slide 1
Demonstration of a ring-FEL as an
EUV lithography tool
Jaeyu Lee, Seunghwan Shin
Pohang Accelerator Laboratory
SSMB Workshop
Dec. 8, 2020

## Slide 2
Contents
Motivation
Target parameters for storage ring based FEL
Ring based FEL - Bypass design
Ring based FEL - Racetrack design
Overview
1
SSMB Workshop

## Slide 3
Motivation
2
Pohang Accelerator Laboratory in Korea is running PLS-II (3 GeV, 282 m storage ring) and PAL-XFEL (10 GeV, 60 Hz XFEL).
Also the project for a construction of low emittance ring about to starts in Korea.
How about storage ring based FEL ?
Motivation : With the advent of the low emittance ring (emittance ~ 100 pm),
normalized emittance become < 1 um.
Advantages : High repetition rate, Stable energy
Disadvantages : Low peak current, Large energy spread
SSMB Workshop
PLS-II
PAL-XFEL

## Slide 4
Target parameters for ring-FEL
3
We started ring-FEL study for the X-ray regime, but it is more suitable for EUV and Water window regimes with a medium energy storage ring.
For a EUV lithography, target parameter is a 1 kW average radiation power at 13.5 nm.
SSMB Workshop

## Slide 5
Ring-FEL : bypass design
4
We started from a low emittance ring designed at 2018.
SSMB Workshop
245 m
150 m
170 m
220 m

## Slide 6
Ring-FEL : bypass design
5
Ring-FEL configuration
SSMB Workshop
Electron Beam Energy = 3 GeV
Circumference = 570 m
Transverse Emittance = 51 pm (round beam, after extraction)
Photon Beam Energy = 0.1 ~ 0.6 keV
(Water window & EUV)
Wait for damping after FEL lasing => repetition rate is order of 10 kHz
Bunch compression is a key point to achive 1 kW power.
N
S
N
S
N
S
N
S
S
N
S
N
S
N
S
N
Extraction
Kicker
Injection
Kicker
100 m
50 m
Bunch
compression
Beamline

## Slide 7
Ring-FEL : bypass design
6
Beam parameters
SSMB Workshop
Beam | E (GeV) |  |  |  |  | 3.000 | 3.000
 | Rms bunch Length (ps) |  |  |  |  | 2.000 | 2.000
 | Charge /bunch Q (nC) |  |  |  |  | 5.0000 | 5.0000
 | Peak current Ip (kA) |  |  |  |  | 1.00 | 1.00
 | Normarized emittance (mm mrad) |  |  |  |  | 0.3000 | 0.3000
 | Emittance (nm rad) |  |  |  |  | 0.0511 | 0.0511
 | Diffraction-limited emit. (nm rad) |  |  |  |  | 1.0742 | 0.1591
 | b in undulator |  |  |  |  | 8.0 | 8.0
 | Beam size sx (mm) |  |  |  |  | 20.22 | 20.22
 | Relative rms energy spread |  |  |  |  | 0.001022 | 0.001022
 | Rms energy spread in terms of rest energy |  |  |  |  | 6.0 | 6.0
Undulator | Period (cm) |  |  |  |  | 4.4000 | 4.4000
 | Magnet full gap (mm) |  |  |  |  | 6.8100 | 18.6000
 | Bu (T) |  |  |  |  | 1.5447 | 0.5025
 | Ku |  |  |  |  | 6.3481 | 2.0652
 | Type |  |  |  |  | Planar | Planar
 | SASE-FEL Wavelength(nm) |  |  |  |  | 13.49926 | 1.99953
 | Photon Energy (keV) |  |  |  |  | 0.09 | 0.62

## Slide 8
Ring-FEL : bypass design
7
Operating using hybrid fill mode
SSMB Workshop
Current
Time
1 turn (~ 2 μs)
Short pulse kick + septum
Hybrid fill mode
Use hybrid fill mode
Extract the beam using a 200-ns short pulse kicker.
The beam after FEL undulator is injected to SR and damped until next extraction.

## Slide 9
Ring-FEL : bypass design
8
Operating using FEL dedicated mode
SSMB Workshop
Use high current 150 bunch mode
Extract the beam using a 2-μs short pulse kicker.
The beam after FEL undulator is injected to SR and damped until next extraction.
Current
Time
~ 30 ns
Short pulse kick + septum
150 camshaft mode
1 turn
. . . . .

## Slide 10
Ring-FEL : bypass design
9
Bunch compression
SSMB Workshop
Extracted bunch current is ~ 100 A. Compression factor should be > 10.
Nominal energy chirping & chicane scheme is hard to apply.
We apply High-Gain Harmonic-Generation (HGHG) scheme.
N
S
N
S
N
S
N
S
S
N
S
N
S
N
S
N
Modulator
N
S
N
S
N
S
N
S
S
N
S
N
S
N
S
N
N
S
N
S
N
S
N
S
S
N
S
N
S
N
S
N
Radiator
Dispersive section
CSR & LSC ON
CSR & LSC OFF

## Slide 11
Ring-FEL : bypass design
10
Limitation – large energy spread and low current
SSMB Workshop

## Slide 12
Ring-FEL : racetrack design
11
No bypass
SSMB Workshop
Electron Beam Energy = 3 GeV
Circumference = 870 m (including two 150 m SS)
Transverse Emittance = 200 pm (round beam)
Photon Beam Energy = 0.1 ~ 0.6 keV
(Water window & EUV)
Operates at equilibrium state => repetition rate is order of 10 MHz
N
S
N
S
N
S
N
S
S
N
S
N
S
N
S
N
100 m
Beamline

## Slide 13
Ring-FEL : racetrack design
12
Beam parameters
SSMB Workshop
Average FEL power = 1 kW
Fill pattern : 5 mA (10 nC) * 80 (Total 400 mA)
Repetition rate = 80 / Revolution time = 42 MHz
RMS bunch length = 14 ps (4.2 mm)
Required FEL peak power
= Average power / {sqrt(2)*RMS bunch length * Rep.rate}
= 1 kW / {sqrt(2)* 14 ps * 42 MHz}
= 0.68 MW
Beam | E (GeV) |  |  |  |  | 3.000
 | Relativistic g |  |  |  |  | 5870.84
 | Magnet rigidity (T-m) |  |  |  |  | 10.00710
 | Rms bunch Length (ps) |  |  |  |  | 14.000
 | (Uniform bunch length ps) |  |  |  |  | 35.093
 | FWHM bunch length (ps) |  |  |  |  | 32.900
 | Rms bunch Length (mm) |  |  |  |  | 4197.200
 | Charge /bunch Q (nC) |  |  |  |  | 10.0000
 | Peak current Ip (kA) |  |  |  |  | 0.28
 | Normarized emittance (mm mrad) |  |  |  |  | 1.2000
 | Emittance (nm rad) |  |  |  |  | 0.2
 | Diffraction-limited emittance (nm rad) |  |  |  |  | 1.0742
 | b in undulator |  |  |  |  | 8.0
 | Beam size sx (mm) |  |  |  |  | 20.22
 | Relative rms energy spread |  |  |  |  | 0.001022
 | Rms energy spread in terms of rest energy |  |  |  |  | 6.0
 | Peak beam power (TW) |  |  |  |  | 0.85
Undulator | Period (cm) |  |  |  |  | 4.4000
 | Magnet full gap (mm) |  |  |  |  | 6.8100
 | Bu (T) |  |  |  |  | 1.5447
 | Ku |  |  |  |  | 6.3481
 | Type |  |  |  |  | Planar, in-vacuum
 | SASE-FEL Wavelength(nm) |  |  |  |  | 13.49926
 | Photon Energy (keV) |  |  |  |  | 0.09
 | Psat (GW) |  |  |  |  | 0.23053
 | Lsat (m) |  |  |  |  | 56.08800
FEL | Peak Brilliance |  |  |  |  | 
 | Photons/sec/mm2/mrad2/0.1% bw |  |  |  |  | 9.185E+30
 | (Peak Brilliance for full transverse coherence) |  |  |  |  | 
 | Repetition rate |  |  |  |  | 4.00E+07
Average radiation power > 1 kW

## Slide 14
Ring-FEL : racetrack design
13
FEL Lasing and target power
SSMB Workshop
1 kW
P(z) (Bunch averaged )

## Slide 15
Ring-FEL : racetrack design
14
P(s) at z = 135 m
SSMB Workshop
10 MW

## Slide 16
Ring-FEL : racetrack design
15
Microbunching after 135 m undulator (avg. power = 1 kW)
SSMB Workshop

## Slide 17
Ring-FEL : racetrack design
16
De-bunched after passing 1 cell lattice
SSMB Workshop

## Slide 18
Ring-FEL : racetrack design
17
Equilibrium parameters of storage ring with FEL lasing (From Z. Huang, NIMA (2008))
SSMB Workshop
1D Power gain length ,
Energy spread increases during the high-gain process
The longitudinal dynamics can be modeled as

## Slide 19
Ring-FEL : racetrack design
18
Equilibrium parameters of storage ring with FEL lasing (From Z. Huang, NIMA (2008))
SSMB Workshop
For a long undulator, we assume the square of equilibrium e spread increases linearly with undulator distance z as , then the equilibrium FEL power becomes
A rough estimate of the maximum equilibrium power is

## Slide 20
Ring-FEL : racetrack design
19
Equilibrium parameters of storage ring with FEL lasing (From Z. Huang, NIMA (2008))
SSMB Workshop
In our case , then
For 1kW average power, ,
then undulator length for 1kW power >> 100 m
Conclusion : We need external seeding power

## Slide 21
Ring-FEL : racetrack design
20
With 10 kW (peak power) external seeding,
1 kW EUV is achieved and equilibrium energy spread is about 0.2 %
SSMB Workshop
We need a seeding radiation with a power of 2% of FEL radiation power.

## Slide 22
Ring-FEL : racetrack design
21
Candidate for external seeding : Regenerative amplifier
SSMB Workshop
H.P. Freund et al., PRAB 16, 010707 (2013)

## Slide 23
Overview
22
Medium-energy storage ring based FEL could provides 1 kW EUV radiation with low emittance ring and regenerative amplifier.
If the radiation wavelength for a lithography moves to soft X-ray, the XFEL in a high-energy storage ring can be a candidate for a lithography tool.
SSMB Workshop

## Slide 24
Thank you
SSMB Workshop